Radioanalytical investigations of uranium concentrations in natural spring, mineral, spa and drinking waters in Hungary

Viktor Jobbágya*, Norbert Kávásia, János Somlaib, Péter Dombováric, Richárd Kardosb, Tibor Kovácsb

aSocial Organization for Radioecological Cleanliness, P.O. Box 158, H-8201 Veszprém, Hungary

bInstitute of Radiochemistry and Radioecology, University of Pannonia, P.O. Box 158, H-8201 Veszprém, Hungary

c Paks Nuclear Power Plant Ltd., P.O. Box 71, H-7031, Paks, Hungary

*Present address: European Commission, Joint Research Centre, Institute for Reference Materials and Measurements (IRMM), Retieseweg 111, B-2440 Geel, Belgium

Environmental Radiation Effects Research Group, National Institute of Radiological Sciences, 4-9-1 Anagawa, Inageku, Chiba 263-8555, Japan

E–mail: Viktor.JOBBAGY@ec.europa.eu

URL: http://irmm.jrc.ec.europa.eu/

Abstract

Within this work, the activity concentrations of uranium isotopes (234U, 235U, and 238U) were analyzed in some of the popular and regularly consumed Hungarian mineral-, spring-, therapeutic waters and tap waters. Samples were selected randomly and were taken from different regions of Hungary (Balaton Upland, Bükk Mountain, Somogy Hills, Mezőföld, Lake Hévíz).

Concentration (mBq L-1) of 234U, 235U, and 238U in the waters varied from 1.1 to 685.2, from <0.3 to 7.9, and from 0.8 to 231.6 respectively. In general, the highest uranium concentrations were measured in spring waters, while the lowest were found in tap waters. In most cases radioactive disequilibrium was observed between uranium isotopes (234U and 238U). The activity ratio between 234U and 238U varies from 0.57 to 4.97.

The calculated doses for the analyzed samples of spring water are in the range 0.07–32.39 Sv y-1 with an average 4.32 Sv y-1.This is well below the 100 Sv y-1 reference level of the committed effective dose recommended by WHO and the EU Council. The other naturally occurring alpha emitting radionuclides (226Ra, 210Po) will be analyzed later to complete the dose assessment. This study provides preliminary information for consumers and authorities about their internal radiological exposure risk due to annual intake of uranium isotopes via water consumption.

Keywords: uranium, alpha spectrometry, natural waters, dose estimation, water quality

Introduction

As many other countries in the Central European region, (e.g. Czech Republic, Slovakia, Romania) Hungary is rich in spring-, thermal-, and mineral waters as well. Recently the consumption of natural mineral- and spring waters comes to be more and more popular in a certain population groups, especially among the adults. It is due to growing concern that components of drinking water may have adverse health effects, and the good publicity of the mineral waters. Furthermore these waters are considered healthier, "more natural", have less unpleasant taste and are less polluted with organic inorganic substances than the tap water itself. It is well known that some of these underground waters have elevated level of dissolved natural radionuclides compared to tap water [1, 2]. Their activity concentration depends on the origin of the water, and varies considerably. In some cases also human activities (fertilizing, mining, water treatment) influence their composition.

According to UNSCEAR [3], drinking water consumption might be a crucial factor in the local exposure to naturally occurring alpha emitting radionuclides, predominantly the members of the 232Th, 238U, and 235U decay series (e.g. 222Rn, 226Ra, 210Po), thus in some cases elevated levels of dose exposure can be expected [4]. Because of this specific health hazard, it is important to control the human consumption of the radioactive waters. In spite of this fact most of the recommendations do not apply to natural mineral waters and to waters that are classified as of medicinal benefit [5, 6]. From health protection point of view, it is of great importance to screen the radioactivity of these waters as well [6].

Earlier, the presence of only 226Ra and 222Rn isotopes have been found in Hungarian drinking waters in concentrations that may be of health concern. Until recently only a few studies on the radioactivity of Hungarian spring waters were published [4, 7, 8], but nowadays an up-dated and more complex survey is available [9].

Our study aims to give preliminary information about the internal radiological exposure risk due to intake of uranium isotopes via water consumption.

Experimental

Sample collection-study area

Samples were selected randomly and were taken from different regions of Hungary (Balaton Upland, Bükk Mountain, Somogy Hills, Mezőföld, Lake Hévíz) as shown in Figure 1.

Fig. 1 Sampling sites in Hungary: 1.) Balf; 2.) Hévíz; 3.) Nemesgulács; 4.) Kékkút; 5.) Igal; 6.)Veszprém; 7.) Balatonfüred; 8.) Felsőörs; 9.) Balatonbozsok; 10.) Óbuda; 11.) Csány 12.) Eger

Table 1 Summary of the origin and types of waters

| Sample code | Origin of water | Region | Type of water |
| --- | --- | --- | --- |
| 1 | Igal, tapwater | Somogy Hills | Drinking water |
| 2 | Igal | Somogy Hills | Therapeutic spa water |
| 3 | Csány, Pannon Aqua | Heves county- Csány | Mineral water |
| 4 | Balf, "Balfi" mineral water | Fertő-Hanság National Park | Mineral water |
| 5 | Óbuda, Norbi Aqua mineral water | Budapest- Óbuda | Mineral water |
| 6 | Veszprém, tap water | Bakony Mountain | Drinking water |
| 7 | Eger tapwater | Bükk Mountain | Drinking water |
| 8 | Eger, József spring | Bükk Mountain | Spring water |
| 9 | Balatonfüred, Kossuth spring | Balaton Upland | Spring water |
| 10 | Balatonfüred, Berzsenyi spring | Balaton Upland | Spring water |
| 11 | Balatonfüred, Szekér Ernő spring | Balaton Upland | Spring water |
| 12 | Kékkút, Theodora spring | Balaton Upland | Spring water |
| 13 | Felsőörs, Felsőörsi spring | Balaton Upland | Spring water |
| 14 | Felsőörs, "Hősök Kútja" spring | Balaton Upland | Spring water |
| 15 | Nemesgulács, Savanyúvíz | Balaton Upland | Spring water |
| 16 | Balatonbozsok, tapwater | Mezőföld | Drinking water |
| 17 | Hévíz, Drinking fountain | Hévíz valley | Spring water |
| 18 | Hévíz, Lake Hévíz | Hévíz valley | Therapeutic spa water |

Balaton Upland

Balaton Upland is situated directly north of Lake Balaton within a line of 20–25 km sampling sites of Nemesgulács, Kékkút, Veszprém, Balatonfüred and Felsőörs are situated in this area.. It is composed mainly by Triassic sediment rocks like dolomite, limestone, and upper Permian red sandstone. There are numerous volcanic cones composed of Pliocene basaltic lava. Dolomite and limestone play an important role as a water reservoir.

Hévíz

One of the oldest and best known medicinal baths in Hungary is found in Hévíz. It is located approximately 5 km from Lake Balaton and has a special climate. The surface area of the Hévíz Lake is 44,479 m2, its average depth is 1-2 m, the spring can be found at the deepest point which is almost 40 m.

The lake itself is fed by so called cold water ((26 oC), and by hot water ((41 oC). The "cold" water can be used for drinking purposes.

Minerals are transported to the surface from a Triassic-age dolomite layer into a spring cave 18 metres in diameter.The sulphurous water contains alkaline hydro-carbonates as well. Benefits of these waters are utilised to cure a number of medical problems.

Eger

Eger is situated at the fall of the Bükk Plateau (Bükk Mountain), which feeds the spring. Szent József Spring – it can be found in the historic centre of Eger town - is low sodium-laden natural mineralwater containing calcium, magnesium and hydrogen carbonite.

Igal

The spa and curative water is alkalic with elevated level of chloride, hydrogen –carbonate and contains iodide as well. The hot curative water is coming from 651 m deep drilled well and its temperature is 76 oC.

Balatonbozsok

Balatonbozsok is situated in the south–west part of Mezőföld region. Tap low carbonate content water comes from a clay loess underground water reservoir through a deep drilled well.

Mineral waters

Balfi mineral water comes from a sediment water reservoir (depth 12-35 m) which consists of limestone sandstone and some marl. Balfi mineral water is rich in carbonic acid and magnesium sulphate, whilst Pannon Aqua and Norbi Aqua contains elevated level of calcium, magnesium and hydrogen carbonate and a lower amount of dissolved material than Balfi. Both of them are from a deep drilled well.

Sampling

All the spring and tap water samples were collected in 5–10 L polypropylene cans; mineral waters were purchased in local supermarkets. The cans were washed with nitric acid before sampling. The collected waters were acidified (pH<2) with concentrated nitric acid to avoid loss of radionuclides by adsorption onto the wall of the can and prevent any biological activities. Spring waters were filtered through a 0.45 μm membrane filter to separate suspended solids. Other waters were not filtered.

Uranium determination

After pouring the acidified sample into a beaker, the water was homogenized by mixing and a known amount of 232U tracer (26.65 mBq) was added and mixed well. Due to the low activity concentrations of uranium isotopes in the water, preconcentration was made prior to their separation by coprecipitation with Fe(OH)3. It was filtered through a 0.1 μm polypropylene membrane filter (Millipore, 0.1 (m, d = 25 mm) the supernatant was discarded and the uranium bearing precipitate was dissolved with 8M HNO3.

Separation of uranium isotopes from other radionuclides was performed using DOWEX 1X8 (100–200 mesh) anionic exchange resin and UTEVA extraction chromatographic resins [10, 11].

Both columns were pre–conditioned with 15 mL 8 M HNO3. UTEVA column was placed immediately below the Dowex 1X8 anion exchange column, so the eluents from the anion exchange column passing directly onto the UTEVA column. The uranium bearing solution (in 8M HNO3) was transferred onto the anion exchange column and passed through both columns, then columns were washed with 8 M HNO3 followed by 3 M HNO3 subsequently and then separated. The UTEVA column was converted into chloride form with 9 M HCl and washed with 5M HCl. Finally the uranium was eluted with 0.02 M HCl and collected into a glass beaker.

Then the purified uranium fraction was electrodeposited as following.

The dry residue was dissolved in 0.75 M H2SO4 and 40% NaHSO4 was added. Samples were evaporated to dryness and re-dissolved in 0.75 M H2SO4, some drops of thymolblue indicator were added and the pH was adjusted (2.1–2.4). The uranium was electrodeposited onto a stainless steel disc for 1.5 h at 1.0 A [12]. Disc was rinsed with alcohol, dried and the measurement of the uranium isotopes was carried out by using high-resolution alpha spectrometry.

The alpha spectrometer (Ordela Soloist) was equipped with passivated ion-implanted planar silicon (PIPS) detectors with an active area of 450 mm2 and 19 keV resolution. The spectra were analysed using WinAlpha freeware software developed by IAEA experts [13]. The counting time was between 60,000 and 100,000 s in general it was set to 86,400 s.

The detection efficiency in the chosen configuration and geometry varied from 22.4-25.7 %. The lower limit of detection (LLD) calculated according to Currie’s method [14] was 0.4 – 0.4 mBq and 0.3 mBq for 234U, 238U, and 235U respectively (for a 160,000 s counting time). Chemical recovery of the uranium was between 78 – 95% with an average of 89%.

Results and discussion

Activity concentration of uranium isotopes

The activity concentrations of uranium isotopes in water samples are presented in Table 2. The total uranium concentration is also given and can be compared with the guidance level for gross alpha activity (500 mBq L-1) recommended by WHO [6].

Table 2 Activity concentration of uranium isotopes in the water samples (mBq L-1)

| Sample code | 238U | 234U | 235U | Σ U isotopes |
| --- | --- | --- | --- | --- |
| 1 | 45.4±1.8 | 51.3±2.1 | <LLD | 96.7±2.7 |
| 2 | 1.3±0.1 | 1.6±0.1 | <LLD | 2.9±0.2 |
| 3 | 19.7±1.2 | 37.1±2.2 | <LLD | 56.8±2.5 |
| 4 | 0.8±0.1 | 1.1±0.1 | <LLD | 1.9±0.1 |
| 5 | 11.9±0.8 | 19.1±1.3 | <LLD | 31±1.6 |
| 6 | 22.2±1.1 | 22.5±1.1 | <LLD | 44.7±1.6 |
| 7 | 27.3±1.4 | 45.1±2.3 | <LLD | 72.4±2.6 |
| 8 | 38.4±1.9 | 21.9±1.1 | <LLD | 60.3±2.2 |
| 9* | 135.2±5.4 | 202.5±8.1 | 4.5±0.2 | 342.2±9.7 |
| 10* | 187.4±5.6 | 189.2±5.7 | 7.6±0.3 | 384.2±8.0 |
| 11* | 231.6±6.9 | 685.2±20.6 | 7.9±0.3 | 924.7±21.7 |
| 12* | 12.1±0.8 | 13.5±0.9 | <LLD | 25.6±1.3 |
| 13* | 5.0±0.5 | 8.7±0.8 | <LLD | 13.7±0.9 |
| 14* | 17.6±1.1 | 18.2±1.1 | <LLD | 35.8±1.5 |
| 15* | 5.9±0.4 | 29.3±1.5 | <LLD | 35.2±1.5 |
| 16 | 1.5±0.1 | 5.2±0.5 | <LLD | 6.7±0.5 |
| 17* | 30.3±1.5 | 28.5±1.4 | <LLD | 58.8±2.1 |
| 18* | 23.2±1.2 | 26.1±1.3 | <LLD | 49.3±1.7 |

*In this case waters were measured earlier as well and results can be found elsewhere for samples 9-15 [9] and for samples 17-18 [15].

Uncertainty is given as combined standard uncertainty, with a coverage factor k=2, corresponding to a level of confidence of 95%. It was below 10 %; typically 4 % (3%–9.5 %).

As shown in Table 2, the activity concentration (mBq L-1) of 234U, 235U, and 238U in the waters varied in a wide range, from 1.1 to 685.2, from <0.3 to 7.9, and from 0.8 to 231.6 respectively. In general, the highest uranium concentrations were measured in spring waters, while the lowest were found in tap waters. The values marked with * in Table 2. well agree with the earlier results [9], within their uncertainty limits.

One of the spring waters exceeds the guidance level for gross alpha activity (500 mBq L-1), whilst two of them are close to it, but most of the waters are far below this value. For comparison, 238U and 234U activity concentrations in waters from various European countries are shown in Table 3. As can be seen, larger span of our data has been found than that in Poland, Bosnia and Herzegovina, Greece and Italy, but some mineral and spring water from Austria contain more dissolved uranium than the analyzed Hungarian waters. In all countries, higher uranium concentrations have been found in spring- and spa waters than in tap water.

Table 3 Summarized data on 238U and 234U activity concentrations in waters from various European countries (mBq L-1)

| Country | 238U | 234U | Reference |
| --- | --- | --- | --- |
| Austria | 1 – 73.6 | 1.4 – 79 | [16] |
|  | 0.72 – 975 | 1.02 – 1251 | [17] |
| Bosnia and Herzegovina | 0.27–16.2 | 0.41 – 15.6 | [18] |
| Greece | 0.91 – 17.27 | 2.13 – 22.01 | [19] |
| Italy | <0.17 – 89.00 | <0.17 – 79.00 | [20] |
| Slovenia | 0.4 mg m−3 ((10.1 mBq L-1)( | [21] |
| Poland | 10.25 – 24.46 | 12.35 – 31.90 | [22] |
|  | 0.5 – 7.7 | 0.5 – 13.6 | [23] |

(Natural uranium was measured

234U/238U isotopic ratio

In most cases radioactive disequilibrium was observed between 234U and 238U in the waters studied. It is well known that in natural waters that the 234U/238U activity ratio can differ from 1, due to environmental processes and human activities as well [24]. After recoil, 234U can be dissolved from rocks and sediments more easily than 238U by complexation with carbonate/hydro-carbonate ions available in the aquatic media. In the analyzed Hungarian waters the 234U/238U activity ratio varies from 0.57 to 4.97 (Figure 2.).

Fig. 2 234U/238U isotopic ratio in water samples

Dose assessment

The activity concentrations of uranium isotopes in different waters were used for estimation of the committed effective dose for adults due the annual intake of these uranium isotopes by water consumption. For this purpose the dose coefficients (Table 4.) recommended by the International Commission of Radiological Protection were used [25]. The annual average consumption of the waters recommended by the WHO [6] 730 L was assumed. It is conservative assumption as most of these waters (e.g. spring and tap waters) are probably consumed only rarely or in smaller amount (0.1–0.5 L d-1) and mostly by adults. In special cases mineral water consumption might exceed 1.5 L d-1 but usually it is still much below 2 L d-1.

Table 4 Dose coefficients for ingestion of uranium isotopes by adult member of the public in Sv Bq−1

| Radionuclide | 238U | 234U | 235U |
| --- | --- | --- | --- |
| Dose coefficients (Sv Bq−1) | 4.5×10−8 | 4.9×10−8 | 4.7×10−8 |

The committed effective dose from 234U, (235U), and 238U intake calculated according to the WHO recommendation can be seen in Figure 3. The internal dose exposures for the analyzed samples of spring water are in the range 0.07–32.39 μSv y-1 with an average 4.32 μSv y-1. 235U will not contribute significantly to the dose due to its low activity concentration.

Fig. 3 Committed effective dose due to uranium intake from water consumption

The total indicative dose (0.1 mSv y-1) recommended by WHO and EC council Directive was not exceeded in any case. The dose contribution due to uranium intake is not significant even if 2 L day-1 water consumption is assumed. However, here it must be noted that other alpha emitting radionuclides (226Ra, 210Po) should be analyzed in order to complete the dose assessment.

Conclusions

234U, 235U, and 238U activity concentrations were determined in water samples (2 therapeutic water, 3 mineral waters, 4 tap waters, 9 frequently consumed spring waters) collected from different regions in Hungary. Uranium concentrations in the analyzed waters vary in a wide range and waters with elevated level of carbonates contain more dissolved uranium than the others. On the basis of the measured values the committed effective dose was calculated according to the WHO recommendation. It can be concluded that the internal dose contribution due to intake of uranium isotopes is not significant. In order to complete the dose assessment the other naturally occurring α emitting radionuclides (226Ra, 210Po) and also the β emitting isotopes (228Ra, 210Pb) should be - and will be - analyzed later. This study provides preliminary information for consumers and authorities about their internal radiological exposure risk due to annual intake of uranium isotopes via water consumption.

Acknowledgements

The authors thank Gábor Szeiler for his assistance in receiving the water samples. Thanks are due to, Nóra Jánoki and József Szabó for their help in collecting samples from Igal and Eger.

References

1. Sánchez AM, Montero MPR, Escobar VG, Vargas MJ (1999) Appl Radiat Isot 50:1049-1055

2. Michael EK, Pravin PP, Miguel AT, Schneider D (2005) J Environ Radioact 80:327-339

3. UNSCEAR (2000) United Nations Scientiﬁc Committee on the Effects of Atomic Radiation (UNSCEAR), Sources and Effects of Ionising Radiation. United Nations, New York.

4. Kovács T, Bodrogi E, Somlai J, Jobbágy V, Dombovári P, Németh Cs (2005) Int Congr Ser 1276:371–372

5. European Communities (1998) Council Directive of 3 November 1998 on the quality of water intended for human consumption (98/83/EC) 32–54

6. WHO (2004) Guidelines for drinking−water quality. 3rd ed. World Health Organization, Geneva, Switzerland.

7. Kovács T, Bodrogi E, Somlai J, Jobbágy V, Patak G, Németh Cs (2003) J Radioanal Nucl Chem 258:191–194.

8. Somlai K, Tokonami S, Ishikawa T, Vancsura P, Gáspár M, Jobbágy V, Somlai J, Kovács T (2007) Radiat Meas 42:491–495

9. Jobbágy V, Kávási N, Somlai J, Máté B, Kovács T (2010) Microchem J 94:159-165

10. Eichrom (2001), Eichrom Technologies, Inc., Analytical procedures-uranium in water- ACW02.

11. Warwick PE, Croudace IW, Dale AA (1999) Appl Radiat Isot 50:579–583

12. Talvitie NA (1972) Anal Chem 44:280–283

13. Noy RC, Garcia-Torano E, Mainegra E, Lopez E (2004) Nucl Instrum Methods Phys Res Sect A 525:522–528

14. Currie LA (1968) Anal Chem 40:586–593

15. Somlai J, Torma Á, Dombovári P, Kávási N, Nagy K, Kovács T (2007) J Radioanal Nucl Chem 272:101–106

16. Wallner G, Wagner R, Katzlberger C (2008) J Environ Radioact 99:1090–1094

17. Gegner M, Irlweck K (2005) Radioactivity in the Environment, 7:135–139

18. Jia G, Belli M, Sansone U, Rosamilia S, Gaudino S (2006) J Environ Radioact 89:172–187

19. Kehagia K, Koukouliou V, Bratakos S, Seferlis S, Tzoumerkas F, Potiriadis C (2007) Desalination, 213:98–103

20. Desideri D, Meli MA, Feduzi L, Roselli C, Rongoni A, Saetta D (2007) J Environ Radioact 94:86-97

21. Kobal I, Vaupotic J, Mitic D, Kristan J, Ancik M, Jerancic S, Skofljanec M (1990) Environ Int 16:141–154

22. Jobbágy V, Chmielewska I, Kovács T, Chałupnik S (2009) Microchem J 93: 200–205

23. Kozlowska B, Walencik A, Dorda J, Przylibski TA (2007) Radiat Meas 42:1380–1386

24. Ivanovich M, Harmon RS (1992) Uranium Series Disequilibrium, Application of Earth, Marine and Environmental Sciences (2nd Edition), Clarendon Press

25. ICRP (1996) Age-dependent Doses to Members of the Public from Intake of Radionuclides: Part 5. Compilation of Ingestion and Inhalation dose Coefficient, Ann ICRP 1996; 26 (1), ICRP Publication 72, Pergamon Press, Oxford.