Preparation of samples for alpha-spectrometry by direct evaporation of extracted species

# Kamila Šťastnáa, b, Vít Fialab, Jan Johna, b

aCentre for Radiochemistry and Radiation Chemistry, Faculty of Nuclear Sciences and Physical Engineering, Czech Technical University in Prague, Břehová 7, 115 19 Prague 1, Czech Republic

bDepartment of Nuclear Chemistry, Faculty of Nuclear Sciences and Physical Engineering,

Czech Technical University in Prague, Břehová 7, 115 19 Prague 1, Czech Republic

e-mail:kamila.stastna@fjfi.cvut.cz, phone: +420 224 358 201, fax: +420 224 358 202

Abstract	Because of the energy loss of α-particles by self-absorption, α-spectrometry requires thin, uniform, and nearly weightless samples. Several methods exist for sample preparation, e.g., electrodeposition or co-precipitation. Unfortunately, the methods yielding the best energy resolution are not always quantitative and are usually relatively demanding and time-consuming. This fact makes application of α-spectrometry for screening tests with radiotracers complicated.

For its simplicity and fastness, the possibility to prepare samples for α-spectrometry by direct evaporation of simple aliquots of aqueous or organic solutions and the influence of the presence of volatile organic diluent or tensioactive agent was investigated. Also, the influence of coating the samples with Mylar film was evaluated. The sample preparation techniques were compared based on the counting efficiency and energy resolution achieved. The performance of the selected method was tested on assessment of the efficiency of americium extraction by BTBP (bis-triazine-bipyridine) extractant.

Keywords	alpha spectrometry, sample preparation, evaporation, americium

Introduction

Alpha spectrometry is a very useful method for analyzing alpha-emitting radionuclides mainly because of its relatively high efficiency and very low background resulting in high sensitivity. Alpha-particle spectrometry is usually performed after a radiochemical separation and deposition of alpha-emitting radionuclides onto a counting surface [1]. In order to obtain the best possible resolution, it is necessary to produce thin, flat, and uniform samples. Techniques for the preparation of sources suitable for alpha spectrometric measurements are reviewed e.g. in [2]. There are three basic methods of alpha-sample preparation: evaporation, co-precipitation, and electrodeposition. In electrodeposition, radioactive material is electrochemically plated from an electrolyte solution onto a polished metal (stainless steel, copper, or other material) cathode planchet, anode being typically platinum wire or gauze. Co-precipitation of actinoides with rare-earth fluorides, followed by filtration on a smooth surface membrane filter of small pore size (0,1-0,2 μm) produces good-quality alpha sources [3]. Direct solution evaporation performs well for small volumes of dilute or electrolyte/carrier free solutions. In this case, the solution is spread uniformly over counting planchet and solvent is evaporated taking care to prevent splattering and consequent contamination of surrounding work area [4]. However, these samples tend to be less uniform. Spreading agents can be added to the solution, but the organics must be removed by firing before measurement. The way of drying the deposited drop of radioactive solution affects the quality of the resulting source significantly. Several drying methods can be used: in open air, in a laminar flow or fume hood, at room temperature or heated under infrared lamp. It is important to make the operation in a dust-free environment to avoid inclusion of dust particles in the radioactive source [5]. The method of direct evaporation has been employed in e.g. [6, 7]. Triethylene glycol may be used as a spreading agent to achieve uniform distribution in samples as e.g. for track registration technique [8]. Another problem associated with counting relatively high-active samples from tracer experiments is that the recoil fragments from alpha-emitting source may cause significant detector contamination. The simplest method to avoid the problem is to use a source coating [9].

The aim of the study was to investigate the influence of sample preparation methods of simple evaporation, evaporation with volatile organic solvent, evaporation in the presence of tensioactive agent, and Mylar coating on counting efficiency and energy resolution in order to select the method suitable for screening tests with trace amounts of radionuclides. The method developed should enable determination of distribution coefficient D in liquid-liquid extraction experiments by direct comparison of the alpha-activities of organic and aqueous phases rather than using the activities of aqueous phases prior to and after the contact with the organic phase which deteriorates the upper and lower limits of detection. The efficiency of the selected method was tested for the case of americium extraction by CyMe4-BTBP molecule in cyclohexanone from nitric acid medium. The BTBP agents, prospective for extraction of actinoides, are described in e.g. [10].

Experimental

Reagents and materials

Sodium carbonate, acetone, tetraethylene glycol, nitric acid, and cyclohexanone were of analytical grade. The solutions of 241Am were prepared by dissolution of americium dioxide AmO2 in 5M HNO3 with subsequent dilutions with distilled water as required. CyMe4-BTBP was supplied by the University of Reading, UK.

The samples were deposited on flat bottom cupped stainless steel planchets with overall diameter 31.8 mm and overall height 2.4 mm (GA-MA & ASSOCIATES, INC., USA). Thin film 3516 Mylar (SPEX SamplePrep, LLC, USA) with thickness of 3 μm was used for sample coating.

Methods

Pretreatment of planchets

Planchets were pretreated by soaking in 20% sodium carbonate solution overnight, washing with distilled and deionized water, rinsing with acetone, and drying under infrared lamp (maximum temperature 80°C).

Sample preparation

Simple evaporation:

10 μL of Am solution was transferred directly onto the pretreated planchet.

Evaporation with acetone:

10 μL of Am solution was pipetted into plastic vial (0.6 mL) and 40 μL of acetone was added followed by mixing with the pipette by aspirating and dispensing the liquid three times before deposition on the planchet.

Evaporation with tetraethylene glycol:

10 μL of Am solution was deposited on the planchet and 4 μL of tetraethylene glycol was added.

All samples were evaporated to dryness under infrared lamp, and heated in flame until glowed with dull red colour. Some samples were coated with Mylar film.

Measurement

Samples were measured using ORTEC® OCTETE Plus Integrated Alpha-Spectroscopy System (ORTEC, Advanced Measurement Technology, Inc., USA) with surface barrier silicon detector NUTRONICS ND.200.20.100 (area 200 mm2), (NUTRONICS, Ltd., UK) at a distance of 16 mm, and the spectra were evaluated by AlphaVision-32 Alpha Analysis Software (ORTEC, Advanced Measurement Technology, Inc., USA).

Extraction experiments

The liquid-liquid extraction experiments were performed by contacting 1 mL of 2M HNO3 (saturated with cyclohexanone) and spiked with 241Am (approx. 3.5 kBq per sample) with 1 mL of 5mM CyMe4-BTBP in cyclohexanone (saturated with 2M HNO3) for 24 hours on laboratory shaker KS 250 basic (IKA® Werke GmbH & Co. KG, Germany) at 250 rpm. Prior to the contact, a 10 µL aliquot was taken as a standard from the 1.01 mL of the aqueous phase prepared. After the contact, the phases were separated by centrifugation for 10 minutes at 4000 rpm and 10 µL aliquots of aqueous and organic phases were taken for the measurement. Samples for alpha-spectrometry were prepared as described above.

Results and discussion

Comparison of sample preparation methods

Fig. 1 and 2 show the influence of sample preparation method on overall count-rate measured and FWHM (full width at half maximum) resolution, respectively. The results, means, theoretical (based on the measured count-rates, only) and/or experimental (calculated from the replicates) standard deviations (σt and σett) of total peak areas and FWHMs are summarized in Tab. 1. The highest count-rate was achieved using simple evaporation method. Lower count-rates in the case of evaporation with acetone can be probably attributed to losses of solution in plastic vial. In the case of evaporation with tetraethylene glycol, lower value of total peak area and higher value of standard deviation may be caused by less uniform spreading of the sample over large area of planchet or possible losses of 241Am during firing. As far as the resolution concerns, it is comparable in simple and with tetraethylene glycol evaporations, but it is about 20 % worse in the case of evaporation with acetone. Further, when compared with the other two methods, the disadvantage of evaporation with tetraethylene glycol is the time needed to evaporate the sample to dryness using infrared lamp. Also, when heating on a hot plate, the samples stream down to one side of planchet when the surface of the plate is not ideally horizontal.

Influence of sample coating

Fig. 3 shows the influence of using Mylar foil coating on the counting efficiency, resolution, and peak position. It can be seen that in the case of coated sample, the energy of the peak is shifted towards lower values by about 400 keV, from 5476 to 5075 keV, the value of FWHM resolution is more than doubled 44,7 vs. 93,7 keV, while the total peak area remains unchanged (within the measurement uncertainty), 930 and 957 counts per 10 minutes.

Extraction experiments

The deposition of standards and aqueous phase on pretreated planchets led to relatively uniform small spreading of samples. On the opposite, deposition of organic phase led to nonuniform spreading over large area of counting planchet. Subsequently, untreated, just brushed to dispose dust, planchets were used for deposition of organic phase leading to more homogenous smaller spreading.

The result of extraction experiments are summarized in Tab. 2 where distribution ratios D = Torg/Taq and D´ = (Tst - Taq)/Taq, calculated from the total peak areas of aliquots of organic (Torg) and aqueous (Taq) phases, or aliquots of standards (Tst) and aqueous phases, are compared. It can be seen that within the experimental uncertainty, the values of D and D´ are identical. Hence, it can be concluded that, if proper care is taken of sample preparation, the efficiency of extraction may be evaluated by simple comparison of the -activities of organic and aqueous phases similarly to the experiments with gamma emitting radionuclides.

Conclusions

Three methods of alpha samples preparation by direct evaporation and the influence on counting efficiency and resolution were compared. The method of simple evaporation of sample without using addition of any substance was evaluated as the fastest and most reproducible for both the aqueous and organic samples. This method was demonstrated to be employable for the evaluation of the efficiency of -nuclides liquid-liquid extraction.

Acknowledgements

This research has been supported by the Ministry of Education, Youth and Sports of the Czech Republic under grant No. MSM 6840770020. L.M. Harwood, F.W. Lewis and M.J. Hudson, School of Chemistry, University of Reading, UK are acknowledged for the supply of CyMe4-BTBP.

References

- Klemenčič H, Benedik L (2010) Appl Radiat Isotopes 68:1247-1251

- Lally AE, Glover KM (1984) Nucl Instrum Methods 223:259-265

- Vajda N, Chang-Kyu K (2010) J Radioanal Nucl Chem 283:203-223

- Choppin G, Baisden P (1978) Radiochemistry. American Chemistry Society, Washington, D.C.

- Sibbens G, Altzitzoglou T (2007) Metrologia 44:71-78

- Küppers G (1998) J Radioanal Nucl Chem 230:167-174

- Koyama S, Mitsugasira T (2008) J Nucl Sci Technol, Supplement 5: 55-64

- Suarey-Navarro MJ et al (2006) Radiat Meas 41:399-404

- Vainblat N et al. (2004) Appl Radiat Isotopes 61:307-311

- Retegan T et al. (2007) Solv Extr Ion Exch 25(4):417-431

Figure captions:

Fig. 1 Comparison of α-sample preparation by evaporation: Total peak area

a simple evaporation

b evaporation with acetone

c evaporation with tetraethylene glycol

Fig. 2 Comparison of α-sample preparation by evaporation: Resolution

a simple evaporation

b evaporation with acetone

c evaporation with tetraethylene glycol

Fig. 3 Spectrum of 241Am for uncoated and Mylar foil coated sample

Table captions

Table 1 Comparison of α-sample preparation by evaporation

Table 2 Extraction of americium by CyMe4-BTBP (aqueous phase: 2M HNO3 spiked with trace amount of 241Am, organic phase: 5mM solution of CyMe4-BTBP in cyclohexanone, shaking time: 24 hrs)

Fig. 1

Fig. 2

Fig. 3

Table 1

| Counts per 10 min FWHM (keV) |
| --- |
| Method | Mean | σe | σt | Mean | σe |
| Simple | 895 | 30 | 30 | 41 | 5 |
| Acetone | 853 | 19 | 29 | 50 | 18 |
| Tetraethylene glycol | 829 | 71 | 29 | 40 | 6 |

σt – theoretical standard deviation (based on the measured count-rates, only)

σe – experimental standard deviation (calculated from the replicates)

Table 2

| Sample | Standard | Organic phase | Aqueous phase |  |  |
| --- | --- | --- | --- | --- | --- |
| No. | total peak area | resolurion | total peak area | resolution | total peak area | resolution | D | D´ |
|  | (counts per 10 min) | FWHM (keV) | (counts per 10 min) | FWHM (keV) | (counts per 100 min) | FWHM (keV) |  |  |
| 1 | 1040 | 33.5 | 904 | 32.4 | 762 | 72.4 | 11.8 | 12.7 |
| 2 | 1018 | 35.3 | 918 | 31.0 | 765 | 50.7 | 12.0 | 12.2 |
| 3 | 1048 | 36.0 | 940 | 31.3 | 778 | 59.9 | 12.1 | 12.4 |
| 4 | 1003 | 34.0 | 909 | 31.6 | 788 | 48.9 | 11.5 | 11.7 |
| mean | 1027 | 34.7 | 918 | 31.6 | 773 | 58.0 | 11.9 | 12.3 |
| σ | 21 | 1.2 | 16 | 0.6 | 12 | 10.8 | 0.3 | 0.4 |

# Text boxes

b

c

a

Mean

+ σ

- σ

Mean

+ σ

- σ

a

b

c