Isolation of generator-produced Ra-223 and Pb-211 in 0.9% NaCl solutions containing EDTA for radiotherapeutic studies

Olga Mokhodoeva, Lidiya Guseva, Nikolay Dogadkin

Vernadsky Institute of Geochemistry and Analytical Chemistry, Russian Academy of Sciences

19 Kosygin Str., Moscow 119991, Russia

olga.mokhodoeva@mail.ru, l.i.guseva@inbox.ru

Tel.: +7(495)9397845, Fax: +7(495)9382054

Abstract

A novel approach to the preparation of the alpha-emitting radionuclide 223Ra was proposed to be applied for treatment of bone metastases and targeted alpha-radioimmunotherapy. The tandem generator system based on ion exchange columns was developed for simultaneous isolation of 223Ra and its daughter 211Pb in the form of stable coexisting 223Ra/211Pb-EDTA complexes in 0.9% NaCl solutions at pH=7.4-8.0. Advantages of the method for routine laboratory and clinical implementation are discussed.

Keywords

Radium-223, alpha-radiopharmaceuticals, radioisotope generators, targeted radiotherapy

Introduction

Alpha-emitting radionuclides are of increasing interest in targeted cancer therapy. The range of alpha particles in tissue is only a few cell diameters (less than 100 μm), offering the possibility of extremely focal irradiation of malignant cells while leaving neighboring cells intact, in particular bone marrow and healthy tissue. Alpha-emitters have greater biological effectiveness than either conventional external beam radiation or beta particles due to high linear energy transfer (LET ˂ 100 keV/μm). Radium-223 is one of the most promising alpha-emitting radionuclides for bone-targeting therapy [1]. A number of recent scientific and clinical investigations are devoted to 223Ra as a treatment of bone metastases occurring when cancer cells (prostate, breast and others) spread from their original site to skeletal surfaces [2-8]. As a calcium mimic and thus a natural bone-seeking agent radium-223 accumulates at areas of increased bone turnover without special carriers. Bone mineral hydroxyapatite, which forms 50% of the bone matrix, is its target. A novel 223Ra-based radiopharmaceutical, named Alpharadin (Algeta ASA, Oslo, Norway), a solution of radium-223 dichloride (223RaCl2) to be administrated intravenously is of particular benefit in the treatment of prostate cancer bone metastases demonstrating not only symptom relief but improvement on overall survival. Alpharadin, marketed as Xofigo, was approved for treatment of patients with castration-resistant prostate cancer by the U.S. Food and Drug Administration (FDA) on 15 May 2013 [9,10].

Radium-223 injected intravenously retains in skeletal metastases realizing in vivo generator of daughter short-lived α-emitters. The 223Ra decay chain is as follows:

A low injected activity is required for therapy because of high energy deposition of 223Ra (28.2 MeV of total energy with 95.3% of the decay energy emitted as alpha-particles). But only the first two ultra short-lived α-emitters 219Rn and 215Po, formed within four seconds of 223Ra decay, would probably rest in the site of the mother radionuclide. The more long-lived radionuclides, primary β-particle emitting 211Pb, and its α-emitting daughters 211Bi/211Po, can escape from the mother vicinity and transferred to another site with blood or plasma flow. Obviously, strong chelating agents, that are able to form stable complexes with radionuclides of the 223Ra decay chain, can be helpful to keep the daughters together with the mother radionuclide. Furthermore, the Ra chelates attached to antibodies or proteins could be used for non-osseous targeted radiotherapy or preparation of novel radiopharmaceuticals.

The most promising approach for routine production of 223Ra in radiochemical laboratories and hospitals is a radioisotope generator method because of the device simplicity, reliability of operating with highly radioactive materials and convenience to be transported. A long-term operating 227Ac/227Th-based generator is usually used for 223Ra production. It represents an extraction chromatographic column containing P,P´-di(2-ethylhexyl)methanediphosphonic acid on silica (Dipex-2 or AC resin) [11]. The common procedure includes separation of 223Ra from parent radionuclides 227Ac/227Th by elution of 223Ra from the generator column with 1M HCl or HNO3. For enhanced separation of 223Ra, two-coupled columns of Dipex-2 are used. The next step is concluded in concentration and final purification of 223Ra by its sorption on the cation-exchange column (AG-50W×12 resin) and subsequent stripping with 8M HNO3. The obtained solution is evaporated and 223Ra residue is dissolved with NaCl/Na3Cit solution [1,11]. The alternative tandem generator system for production and on-line isolation of 223Ra in complexing forms were developed in our previous works. The system consists of two columns: the anion-exchange generator column with loaded 227Ac/227Th-source from which 223Ra is separated with an aqueous-alcoholic solution and the cation-exchange column intended to prepare 223Ra solution suitable for biomedical use [12,13].

The goal of the present work was to determine the conditions for simultaneous isolation of 223Ra and its daughter 211Pb in the form of stable coexisting 223Ra/211Pb-EDTA complexes in NaCl solutions using the cation-exchange method. A scheme for on-line production of 223Ra as a radiopharmaceutical for direct intravenous administration to treat bone metastases as well as for targeted radioimmunotherapy was suggested.

Experimental

## Reagents and equipment

HNO3, CH3OH, NaCl, Na2EDTA, NH4OH («Acros Organics») were of analytical grade. Stock NaCl and Na2EDTA solutions were prepared by dissolution of a weighed reagent portion in double-distilled water or 0.9% NaCl (for Na2EDTA). Dowex-1(8 strong base anion-exchanger and Dowex-50(8 strong acid cation-exchanger of 100-200 mesh («Serva») were placed into glass columns (0.3-0.5 ( 5-10) cm and used as generator and for elution experiments.

The pH of Na2EDTA solutions was adjusted with NH4OH or HNO3 and measured with a pH-meter (HANNA Instruments).

Alpha-activities of the radionuclides were measured using an a-Analyst Spectrometer from Canberra. Gamma-activities were measured with a NaI(Tl) crystal. Gamma-spectrometric determination of radionuclides was carried out with a high-purity Ge detector from Canberra and resolution of 2keV at 1332 keV. The spectra were analysed using the Genie-2000 Spectra Analysis Software. The radiochemical purity of short-lived radionuclides was also controlled by measuring the half-lives. 227Ac was identified through the measurement of γ lines of the 227Th daughter radionuclide after its accumulation for several days.

## Generator system and procedures

Radium-223 was regularly produced using the 227Ac-based generator described earlier [14]. Briefly, 227Ac was loaded on the column filled with 0.5 g of Dowex-1(8 anion-exchanger utilized as generator of 223Ra since 2002. Aqueous methanol-nitric acid solutions (0.70-0.75M HNO3 - 80% CH3OH) were used as eluents for separation of 223Ra from 227Ac/227Th. No breakthrough of the parent radionuclides 227Ac and 227Th in the eluate was observed (Fig. 1). The purification coefficient of 223Ra from 227Ac/227Th was (106.

Fig. 1 α-Spectra of 227Ac (aliquot) loaded on generator column 13.11.2002 (a) and 223Ra in 0.7M HNO3-80% CH3OH solution after elution from generator column 02.12.2013 (b).

The solution obtained from the generator containing 223Ra in 0.70-0.75M HNO3 - 80% CH3OH was passed through the column with 0.05 g of Dowex-50(8 cation-exchanger which completely retains radium. Investigation of 223Ra elution from the cation-exchange column was carried out with saline solutions (0.9% NaCl) containing disodium salt of ethylenediaminetetraacetic acid (Na2EDTA) in the range of concentration from 0.001 to 0.1M, at pH=4.5-8. A special preliminary procedure was developed to precondition the column before elution: after sorption of 223Ra from HNO3 aqueous-alcoholic solution the column was subsequently washed with 2 mL of double-distilled water and 4 mL of 0.9% NaCl. After each sorption-elution cycle the cation-exchange column was washed with 2 mL of 2M HNO3, large amounts of double-distilled water (until pH(6) and then saturated with 0.70-0.75M HNO3 - 80% CH3OH solution. Solutions were passed through the column at a flow rate 0.2-0.3 ml/min in all experiments.

Results and discussion

The studies on 223Ra/211Pb isolation were carried out using normal saline solutions (0.9% NaCl or 0.15M NaCl), which are usually used for intravenous injection. Previously the cation-exchange behavior of radium and lead in saline solutions was studied. It was found that both 223Ra and 211Pb are strongly retained by Dowex-50(8 cation-exchanger in NaCl solutions when [NaCl]≤0.2M, the distribution coefficients are more than n·103 g/mL. Thus, 223Ra/211Pb can not be eluted from the cation-exchange column by normal saline solution.

The Na2EDTA-NaCl solutions were studied as eluents for 223Ra/211Pb isolation in the present investigation.

Isolation of 223Ra and  211Pb/211Bi in 0.9% NaCl solutions containing Na2EDTA

In previous work the cation-exchange behavior of 223Ra and 211Pb/211Bi as EDTA and DTPA complexes in aqueous solutions were studied. It was shown that 211Pb/211Bi could be separated from 223Ra at the range of pH=2.5-7.0, while 223Ra could be eluted from the cation-exchange column at pH(9 [12,13].

Comparative data on elution of radium-223 and lead-211 with aqueous and saline Na2EDTA solutions at different pH values are presented in Fig. 2.

Fig. 2 Elution of 211Pb (circles) and 223Ra (squares) with 0.05M Na2EDTA vs pH: aqueous solutions (empty), saline 0.15M NaCl solutions (filled); Dowex-50x8, 0.05 g

It can be seen in both aqueous and saline solutions that 211Pb is eluted at lower pH values compared with 223Ra. In the case of NaCl solutions radium starts to wash out at pH=6.2 and its almost complete elution is achieved at pH(7.2 while in the absence of NaCl for Ra elution the pH value of the eluent should be not less than 9.

As mentioned above, the main goal of this work was to determine conditions when both 223Ra and 211Pb would be eluted simultaneously in the form of coexisting 223Ra/211Pb-EDTA complexes. The binding of both 223Ra and 211Pb presumably allows daughter radionuclides to be retained within mother site preventing spread of daughters to not-targeting organs.

The data on 223Ra elution with saline Na2EDTA solutions as a function of [Na2EDTA] are presented in Fig. 3.

More than 90% of radium is eluted in 1 ml when the Na2EDTA concentration is ≥0.05M. For the further studies the 0.05M Na2EDTA-0.15M NaCl solution was chosen as eluent.

Fig. 3 Elution of 223Ra vs Na2EDTA concentration; 0.15M NaCl; pH≈7.4; Dowex-50x8, 0.05 g

It is known that biologic systems are characterized by definite pH values, e.g. the normal pH of blood is 7.4. To determine optimal conditions for 223Ra isolation in the form suitable for biomedical trials we studied elution of 223Ra/211Pb-EDTA complexes in the range of pH closed to 7-8. The elution curves of 223Ra/211Pb-EDTA with 0.05M Na2EDTA-0.15M NaCl solution at pH values from 6.99 to 8.04 are presented in Fig. 4.

Fig. 4 Elution curves of 223Ra/211Pb with 0.05M Na2EDTA-0.15M NaCl at pH value: 6.99 (1), 7.21 (2), 7.42 (3), 7.63 (4), 7.75 (5), 8.04 (6); Dowex-50x8, 0.05 g

As it is shown at pH=7.4-8.0 more than 90% of 223Ra/211Pb are eluted from the column with 1 mL of the 0.05M Na2EDTA-0.15M NaCl solution. The higher pH of the eluent the lower volume is needed for quantitative 223Ra/211Pb elution (0.5 mL is enough at pH=7.6-8.0). Special experiments on repeated passing of the eluate through the same cation-exchange column (preconditioned appropriately) were carried out. The obtained elution curves were identical to the curves presented in Fig. 4. It allows concluding, that sufficiently stable 223Ra/211Pb-EDTA complexes are formed in the 0.05M Na2EDTA-0.15M NaCl at investigated pH range.

Based on the obtained data a simple and effective method for 223Ra production from anion-exchange generator column and subsequent isolation of stable 223Ra/211Pb complexes using cation-exchange column was developed. The scheme of the method is presented in Fig. 5.

Fig. 5 The scheme of 223Ra production using anion-exchange generator column and subsequent isolation of 223Ra /211Pb in saline solutions using cation-exchange column

The final saline 223Ra/211Pb-EDTA solution does not contain any other radionuclides except radium-223 and its daughters. A γ-spectrum of the 223Ra/211Pb eluate in 0.05M Na2EDTA-0.15M NaCl solution at pH=7.4 from Dowex-50x8 cation-exchange column is shown in Fig. 6.

Fig. 6 γ-Spectrum of 223Ra in 0.05M Na2EDTA-0.15M NaCl solution at pH=7.4 after elution from Dowex-50x8, 0.05 g

Conclusions

- The cation-exchange behavior of 223Ra and 211Pb in NaCl-Na2EDTA solutions in dependence on composition of solution, concentration of complexing agent and pH value was studied.

- The optimal conditions for 223Ra/211Pb elution in the form of their coexisting complexes with Na2EDTA in 0.9% NaCl solutions were determined.

- A novel scheme of 223Ra preparation using tandem generator system for targeted alpha-radiotherapy was developed. The scheme is adaptable to automation for the routine clinical process, excludes the need of evaporation of the high acid radioactive solutions reducing hazards to technical staff.

- The extension study of 223Ra/211Pb isolation with various eluents using the developed scheme is being carried out and will be presented in the future.

Acknowledgments

The authors are very grateful to Head of the Laboratory of Radiochemistry GEOKHI RAS Dr. Yury M. Kulyako for helpful discussions and support; Dr. Dmitry A. Malikov and Dr. Trofim I. Trofimov for kind help with the alpha-spectrometric measurements.

References

# Comments

I think Pb-211 should also be included in the title, as this is the essence of the work presented

This can be slightly misleading, the patients doesn’t survive but live a few months longer.

rephrase; strange use of words

Cit=?

This should be written the first time this abbreviation is used, not here.

Reference here, if these are previous studies

What is the difference from your previous studies, reference 12? (it’s in Russian so most (including me) can’t read it) I think this must be further clarified.

Will Pb-211 formed from the decay of Ra-223 after elution also be retained in the complex? This should be investigated (if not done already), otherwise Pb-generated in vivo can still escape in the body and then it would be simpler to inject the pure radium…

Write as text, not a list.

# Endnotes

. Henriksen G, Breistøl K, Bruland ØS, Fodstad Ø, Larsen RH (2002) Significant Antitumor Effect from Bone-seeking, α-Particle-emitting 223Ra Demonstrated in an Experimental Skeletal Metastases Model. Cancer Res 62:3120-3125.

. Nilsson S, Larsen RH, Fossa SD, Balteskard L, Borch KW, Westlin J-E, Salberg G, Bruland ØS (2005) First Clinical Experience with α-Emitting Radium-223 in the Treatment of Skeletale Metastases. Clin Cancer Res 11:4451-4459.

. Larsen RH, Saxtorph H, Skydsgaard M, Borrebaek J, Jonasdottir TJ, Bruland ØS, Klastrup S, Harling R, Ramdahl T (2006) Radiotoxity of the Alpha-emittng Bone-seeker 223Ra Injected Intravenously into Mice: Histology, Clinical Chemistry and Hematology. In Vivo 20:325-332.

. Bruland ØS, Nilsson S., Fisher DR, Larsen RH (2006) High-Linear Energy Transfer Irradiation Targeted to Skeletal Metastases by the α-Emitter 223Ra: Adjuvant or Alternative to Conventional Modalities? Clin Cancer Res 12:6250s-6257s.

. Harrison MR, Wong TZ, Armstrong AJ, George DJ (2013) Radium-223 chloride: a potential new treatment for castration-resistant prostate cancer patients with metastatic bone disease. Cancer Manag Res 5:1-14.

. Carrasquillo JA, O’Donoghue JA, Pandit-Taskar N, Humm JL, Rathkopf DE, Slovin SF, Williamson MJ, Lacuna K, Aksnes A-K, Larson SM, Scher HI, Morris MJ (2013) Phase I pharmacokinetic and biodistribution study with escalating doses of 223Ra-dichloride in men with castration-resistant metastatic prostate cancer.  Eur J Nucl Med Mol Imaging 40:1384-1393.

. Jadvar H, Quinn DI (2013) Targeted α-Particle Therapy of Bone Metastases in Prostate Cancer. Clin Nucl Med 38:966-971.

. Parker C, Nilsson S, Heinrich D, Helle SI, O’Sullivan JM, Fossa SD, Chodacki A, Wiechno P, Logue J, Seke M, Widmark A, Johannessen DC, Hoskin P, Bottomley D, James ND, Solberg A, Syndikus I, Kliment J, Wedel S, Boehmer S, Dall'Oglio M, Franzén L, Coleman R, Vogelzang NJ, O'Bryan-Tear CG, Staudacher K, Garcia-Vargas J, Shan M, Bruland ØS, Sartor O for the ALSYMPCA Investigators (2013) Alpha Emitter Radium-223 and Survival in Metastatic Prostate Cancer. N Engl J Med 369:213-223.

. Wissing MD, FWB van Leeuwen, G van der Pluijm, Gelderblom H (2013) Radium-223 Chloride: Extending Life in Prostate Cancer patients by treating Bone Metastases. Clin Cancer Res 19:5822-5827.

. Xofigo product information (2013) U.S. Xofigo Web site: www.xofigo-us.com/product-information/ Accessed 18 Nov 2013.

. Henriksen G, Hoff P, Alstad J, Larsen RH (2001) 223Ra for endoradiotherapeutic applications prepared from an immobilized 227Ac/227Th source. Radiochim Acta 89:661-666.

. Guseva LI, Dogadkin NN (2008) A tandem generator for production and isolation of short-lived  α-radionuclides  Ra, Pb and Bi in EDTA solutions.  Radiochemistry 50:310-315.

. Guseva LI (2009) A tandem generator system for production of 223Ra and 211Pb/211Bi in DTPA solutions suitable for potential application in radiotherapy. J Radioanal Nucl Chem 281:577-583.

. Guseva LI, Tikhomirova GS, Dogadkin NN (2004) An 227Ac-211Pb generator for test experiments of solution chemistry of element 114. J Radioanal Nucl Chem 260:167-172.

# Text boxes

223Ra(11.43d) → 219Rn(3.96s) → 215Po(1.78ms) → 211Pb(36.1m) → 211Bi(2.14m) → 211Po(0.52s)

α↓                      α↓

207Tl(4.77m) → 207Pb stab.

α

β

β

α

α

β

a

b

227Ac/227Th

0.7M HNO3 - 80% CH3OH

Dowex 1(8

Dowex 50(8

223Ra

0.05M Na2EDTA in

0.9% NaCl; pH=7.4-8.0

Saline solution of 223Ra/211Pb-EDTA

Radiotherapeutic application